## Slide 1: Digital transmission
Sharada Valiveti
Chandan Trivedi
Parita Oza
Umesh Bodkhe

## Slide 2: Contents
Digital to Digital Conversion
Analog to Digital Conversion
Transmission Modes

## Slide 3: Digital Transmission
Information needs to be converted into either a digital signal or an analog signal
Here, we study schemes and techniques for digital transmission
Digital to Digital Conversion: Converting Digital Data into Digital Signals
Analog to Digital Conversion: Changing Analog signal into digital signal
Transmission Modes: Deciding Serial or Parallel Transmission of data

## Slide 4: Digital-to-Digital Conversion
Line Coding Line Coding Schemes Block Coding Scrambling

## Slide 5: Line Coding
Process of converting digital data (in bits) to digital signals is called the Line Coding
Line Coding and Decoding

## Slide 6: Line Coding: Common Characteristics
Signal Element Versus Data Element
  Data element is the smallest entity that can represent a piece of information (this is the bit)
  Signal element carries data elements and is the shortest unit of a digital signal
  Wish to send data element
  Can send signal element
  Data elements are being carried
  Signal elements are the carriers
Define ratio r as the number of data elements carried by one signal element

## Slide 7
Signal Element Vs. Data Element

## Slide 8: Line Coding: Common Characteristics
Data Rate Versus Signal Rate
  Data rate defines number of data elements (bits) sent in 1 second (bps)
  Signal rate is the number of signal elements sent in 1 second (baud)
  Data rate is also called bit rate
  Signal rate is called a pulse rate or modulation rate or the baud rate
Goal of the data communications is to increase data rate while decreasing signal rate
Increasing data rate increases speed of transmission
Decreasing signal rate decreases the bandwidth requirement

## Slide 9
Given S is the Signal Rate, N is the Data Rate (bps)
S = N / r
3 cases are possible:
  c is case factor, which varies for the best, average and worst cases
  Best case - we need minimum signal rate
  Average case – we are interested in
  Worst case – we need maximum signal rate
  Save = c X N X (1/r) baud

## Slide 10: A signal is carrying data in which one data element is encoded as one signal element ( r = 1). If the bit rate is 100 kbps, what is the average value of the baud rate if c is between 0 and 1?
Solution
We assume that the average value of c is 1/2 . The baud rate is then

## Slide 11: Line Coding: Common Characteristics
Bandwidth
  Digital signal is nonperiodic
  Bandwidth of nonperiodic digital signal is continuous and theoretically infinite
  Effective bandwidth is finite
  Baud rate and not the bit rate determines the required bandwidth for a digital signal
  More changes in signal means injecting more frequencies into signal
  Range of bandwidth and Amplitude are also important, rather than its value
Although the actual bandwidth of a digital signal is infinite, the effective bandwidth is finite.

## Slide 12
Minimum Bandwidth can be given as –
Bmin = c X N X (1/r)
Maximum data rate is
Nmax = (1/c) X B X r

## Slide 13: The maximum data rate of a channel (see Chapter 3) is Nmax = 2 × B × log2 L (defined by the Nyquist formula). Does this agree with the previous formula for Nmax?
Solution
A signal with L levels actually can carry log2L bits per level. If each level corresponds to one signal element and we assume the average case (c = 1/2), then we have

## Slide 14: Line Coding: Common Characteristics
Baseline Wandering
  Receiver calculates a running average of the received signal power
  This average is called Baseline
  Incoming signal is evaluated against this baseline to determine the value of the data element
  A long string of 0s or 1s can cause a drift in the baseline (baseline wandering)
    Receiver cannot decode the information correctly
  Hence prevent baseline wandering

## Slide 15: Line Coding: Common Characteristics
DC Components
  When the voltage level in a digital signal is constant for a while, the spectrum creates very low frequencies
  These frequencies (around zero) are called DC (direct-current) components
    Present problems for a system that cannot pass low frequencies or that uses electrical coupling
  DC component is 0/1 parity that can cause base-band wandering

## Slide 16: Line Coding: Common Characteristics
Self – synchronization
  Receiver’s bit intervals must correspond exactly to the sender’s bit intervals to interpret the signals correctly
Effect of Lack of Synchronization

## Slide 17
In a digital transmission, the receiver clock is 0.1 percent faster than the sender clock. How many extra bits per second does the receiver receive if the data rate is 1 kbps? How many if the data rate is 1 Mbps?
Solution
At 1 kbps, the receiver receives 1001 bps instead of 1000 bps.
At 1 Mbps, the receiver receives 1,001,000 bps instead of 1,000,000 bps.

## Slide 18: Line Coding: Common Characteristics
Built-in Error Detection
  Used to detect some or or all of the errors that occurred during transmission
Immunity to Noise and Interference
  Code should be immune to noise and other interferences
Complexity
  Costly to implement than a simple one
    A signal that uses four signal levels is more difficult to interpret than one that uses only two levels

## Slide 19: Line Coding Schemes
5 Categories

## Slide 20: Line Coding Schemes: Unipolar
All signal levels are on one side of the time axis, either above or below
Designed as a Non-Return-to-Zero (NRZ) scheme
  Positive voltage defines bit 1 and the zero voltage defines bit 0
NRZ – signal does not return to zero at the middle of the bit
Scheme is costly
  The normalized power (power needed to send 1 bit per unit line resistance) is double
  Hence not used in communications these days

## Slide 21
Unipolar NRZ Scheme
Scheme is prone to baseline wandering and DC components.
It has no synchronization or any error detection.
It is simple but costly in power consumption.

## Slide 22: Line Coding: Polar
Voltages are on both sides of the time axis
Voltage level for 0 can be positive and the voltage level for 1 can be negative
Non-Return-to-Zero
  2 Versions
    Non-Return-to-Zero Level (NRZ-L) – Positive Voltage for one symbol and negative for the other
    Non-Return-to-Zero Invert (NRZ-I) – the change or lack of change in polarity determines value of symbol
  Baseline wandering is common problem
    Twice as severe in NRZ-L
  Sender/receiver clock synchronization issues
    More serious in NRZ-L
  Vulnerable to sudden change of polarity in the system
NRZ-L and NRZ-I both have an average signal rate of N/2 Bd.

## Slide 23: A system is using NRZ-I to transfer 1-Mbps data. What are the average signal rate and minimum bandwidth?
Solution
The average signal rate is S= c x N x R = 1/2 x N x 1 = 500 kbaud.
The minimum bandwidth for this average baud rate is Bmin = S = 500 kHz.
Note c = 1/2 for the avg. case as worst case is 1 and best case is 0

## Slide 24
Polar NRZ-L and NRZ-I schemes
In NRZ-L the level of the voltage determines the value of the bit. In NRZ-I the inversion or the lack of inversion determines the value of the bit.

## Slide 25: Line Coding: Polar
Return to Zero
  Uses 3 values – Positive, Negative and Zero
  Signal changes not between the bits but during the bit
  Requires two signal changes to encode a bit and therefore occupies greater bandwidth
  No DC component
  More complex to create and discern as 3 levels
  Hence not used these days
  Replaced by Manchester and Differential Manchester schemes

## Slide 26
Polar RZ Scheme

## Slide 27: Line Coding: Polar
Biphase
  Manchester and Differential Manchester
  Manchester Encoding has idea of NRZ-L and RZ
  Differential Manchester Encoding combines idea of NRZ-I and RZ
  No baseline wandering
  No DC component
  Signal rate is double than that for NRZ
    There is always one transition at the middle of the bit and may be one transition at the end of each bit

## Slide 28
Polar Biphase: Manchester and Differential Manchester Schemes
In Manchester and differential Manchester encoding, the transition
at the middle of the bit is used for synchronization.

## Slide 29: Line Coding: Bipolar
Also called multilevel binary
3 voltage levels – Positive, Negative, Zero
  Voltage level for one data element is at zero, voltage level for other element alternates between positive and negative
AMI (Alternative Mark Inversion) and Pseudoternary

## Slide 30: Line Coding: Bipolar
Same signal rate as NRZ
No DC component
Concentration of energy is found around frequency N/2
AMI is commonly used for long –distance communication
  Has synchronization problem when a long sequence of 0s is present in the data

## Slide 31: Line Coding: Multilevel Schemes
Goal is to increase the number of bits per baud by encoding a pattern of m data elements into a pattern of n signal elements
  Group m data elements to produce a combination of 2m data patterns
  If there are L levels, Ln combinations of signal patterns can be produced
  If 2m = Ln, each data pattern is encoded in one signal pattern
  If 2m < Ln, data patterns occupy only a subset of signal patterns
  This subset can be carefully designed to prevent baseline wandering, provide synchronization and to detect errors that occurred during transmission
  Data encoding is not possible if If 2m > Ln, because some data patterns cannot be encoded

## Slide 32: Line Coding: Multilevel Schemes
Codes are classified as mBnL
  m is length of binary pattern
  B means binary data
  n is length of signal pattern
  L is number of levels in the signalling
2B1Q – two binary, one quaternary
8B6T – eight binary, six ternary
4D – PAM5 – four-dimensional five level pulse amplitude modulation

## Slide 33
Multilevel: 2B1Q – used in Digital Subscriber Line (DSL)

## Slide 34
In the 2B1Q scheme, we have no redundancy and we see that a DC component is present.
If we use a code with redundancy we can decide to use only “0” or “+” weighted codes (more +’s than -’s in the signal element) and invert any code that would create a DC component. E.g. ‘+00++-’ -> ‘-00--+’
Receiver will know when it receives a “-” weighted code that it should invert it as it doesn’t represent any valid symbol

## Slide 35
Multilevel: 8B6T – used with 100BASE-4T Cable
No. of data patterns = 2^8 = 256
L = 3
Signal elements = 6
Signal patterns possible = 3^6 = 729
Redundant signals = 729 – 256 = 473
  Provide synchronization and error detection
  Used to provide DC balance

## Slide 36
Average Signal rate Save = ½ X N X 6/8
Minimum bandwidth is close to 6N/8
Each signal has weight 0 or +1 DC values
  No pattern with weight of -1
  To create DC balance, sender inverts the actual signal
  Receiver can easily recognize the inverted pattern as the weight is -1

## Slide 37
Multilevel: 4D-PAM5 Scheme – used in Gigabit LANs

## Slide 38
In some cases, we split the signal transmission up and distribute it over several links.
The separate segments are transmitted simultaneously. This reduces the signaling rate per link -> lower bandwidth.
This requires all bits for a code to be stored.
xD: means that we use ‘x’ links
YYYz: We use ‘z’ levels of modulation where YYY represents the type of modulation (e.g. pulse amplitude modulation - PAM).
Codes are represented as: xD-YYYz

## Slide 39: Line Coding: Multitransition: MLT-3
Uses 3 levels: +V, 0 and –V
Three transition rules
  If the next bit is 0, there is no transition
  If the next bit is 1 and the current level is not 0, the next level is 0
  If the next bit is 1 and the current level is 0, the next level is the opposite of the last nonzero level

## Slide 40
Multitransition: MLT-3 Scheme

## Slide 41
Signal rate is same as NRZ-I
Because of the resulting bit pattern, we have a periodic signal for worst case bit pattern: 1111
This can be approximated as an analog signal a frequency 1/4 the bit rate!

## Slide 43: Block Coding
Block codes provide redundancy and improves performance of line coding
  Redundancy is needed for synchronization and providing some kind of inherent error detecting
Block coding changes a block of m bits into a block of n bits
  n > m
Referred to as mB/nB encoding technique involves 3 steps
  Division – sequence of bits is divided into m-bits
  Substitution – substitute an m-bit group with an n-bit group
  Combination – n-bit group is combined to form a stream
The new stream has more bits than the original bits
Block coding is normally referred to as mB/nB coding;
It replaces each m-bit group with an n-bit group

## Slide 44
Block Coding Concept
The resulting bit stream prevents certain bit combinations that when used with line encoding would result in DC components or poor synchronization quality

## Slide 45
Using Block Coding 4B/5B with NRZ-I line coding scheme
Issues with NRZ-I (Revisited):
Synchronization problem – a long sequence of 0s can make receiver clock lose synchronization
Resolved with 4B/5B encoding:
Block coded stream does not have more than 3 consecutive zeros

## Slide 46
4B/5B Mapping codes

## Slide 47
Substitution in 4B/5B block coding
Redundancy:
A 4 bit data word can have 24 = 16 combinations
A 5 bit word can have 25 = 32 combinations
No. of extra words = 32 – 16 = 16
Some of these extra words are used for control/signaling purposes

## Slide 48: We need to send data at a 1-Mbps rate. What is the minimum required bandwidth, using a combination of 4B/5B and NRZ-I or Manchester coding?
Solution
First 4B/5B block coding increases the bit rate to 1.25 Mbps.
The minimum bandwidth using NRZ-I is N/2 or 625 kHz.
The Manchester scheme needs a minimum bandwidth of 1.25 MHz.
The first choice needs a lower bandwidth, but has a DC component problem;
The second choice needs a higher bandwidth, but does not have a DC component problem.

## Slide 49
8B/10B Block Encoding
More the bits – better the error correction:
No. of redundant bits = 210 – 28 = 768
The 8B10B block code adds more redundant bits
Thereby choose code words that would prevent a long run of a voltage level that would cause DC components

## Slide 50: Scrambling
Biphase schemes are not suitable in long distance communications due to wide bandwidth requirement
Combination of block codes and NRZ line coding are not suitable for long distance communications due to the of DC component
Bipolar AMI are preferred for long distances
  Scrambling offers for a solution that does not increase number of bits and does provide synchronization
  Modifies part of the AMI rule to include scrambling
  System inserts required pulses based on the defined scrambling rules
  Two common scrambling techniques
    B8ZS
    HDB3

## Slide 51
AMI used with Scrambling

## Slide 52
B8ZS substitutes eight consecutive zeros with 000VB0VB.
The V stands for violation, it violates the line encoding rule
B stands for bipolar, it implements the bipolar line encoding rule
Two cases of B8ZS Scrambling

## Slide 53
HDB3 substitutes four consecutive zeros with 000V or B00V depending
on the number of nonzero pulses after the last substitution.
If # of non zero pulses is even the substitution is B00V to make total # of non zero pulse even.
If # of non zero pulses is odd the substitution is 000V to make total # of non zero pulses even.

## Slide 54: Analog-to-Digital Conversion
Pulse Code Modulation
Delta Modulation

## Slide 55: Pulse Coded Modulation (PCM)
PCM is the most common technique to change an analog signal into digital (digitization)
PCM encoder has 3 processes
  Sampling – analog signal is sampled
  Quantization – analog signal is quantized
  Encoding – quantized values are encoded as stream of bits

## Slide 56
Components of the PCM Encoder

## Slide 57: PCM (Sampling)
Analog signal is sampled every TS secs
  Ts is the sample interval or period
    Inverse is called Sampling Rate or Sampling frequency (fs)
Three sampling methods:
  Ideal - an impulse at each sampling instant
    Cannot be easily implemented
  Natural - a pulse of short width with varying amplitude
    High-speed switch is turned on for a small period
  Flat-top - sample and hold, like natural but with single amplitude value
    Most common method created using a circuit
The process is referred to as pulse amplitude modulation PAM and the outcome is a signal with analog (non integer) values

## Slide 58
3 different Sampling Methods for PCM

## Slide 59: PCM: Sampling Rate
Nyquist Theorem
  To reproduce the original analog signal, one necessary condition is that the sampling rate be at least twice the highest frequency in the original signal
  Sampling can be done only if the signal is band-limited
  Sampling rate must be 2 times the highest frequency; not the bandwidth
Nyquist sampling rate for low-pass and bandpass signals

## Slide 60: For an intuitive example of the Nyquist theorem, let us sample a simple sine wave at three sampling rates: fs = 4f (2 times the Nyquist rate), fs = 2f (Nyquist rate), and fs = f (one-half the Nyquist rate).
Recovery of a sampled sine wave for different sampling rates
Sampling at the Nyquist rate can create a good approximation of the original sine wave
Fig. b and Fig. c does not produce the original signal

## Slide 61
Consider the revolution of a hand of a clock.
The second hand of a clock has a period of 60 s.
According to the Nyquist theorem, we need to sample the hand every 30 s (Ts = T or fs = 2f ).
  In part a, the sample points, in order, are 12, 6, 12, 6, 12, and 6.
  The receiver of the samples cannot tell if the clock is moving forward or backward
In part b, we sample at double the Nyquist rate (every 15 s). The sample points are 12, 3, 6, 9, and 12.
  The clock is moving forward
In part c, we sample below the Nyquist rate (Ts = T or fs = f ).
  The sample points are 12, 9, 6, 3, and 12.
  Although the clock is moving forward, the receiver thinks that the clock is moving backward.

## Slide 62
Sampling of the clock with only one hand

## Slide 63
An example related to seemingly backward rotation of the wheels of a forward-moving car in a movie. This can be explained by under-sampling. A movie is filmed at 24 frames per second. If a wheel is rotating more than 12 times per second, the under-sampling creates the impression of a backward rotation
Telephone companies digitize voice by assuming a maximum frequency of 4000 Hz. The sampling rate therefore is 8000 samples per second
A complex low-pass signal has a bandwidth of 200 kHz. What is the minimum sampling rate for this signal?
Solution
The bandwidth of a low-pass signal is between 0 and f, where f is the maximum frequency in the signal. Therefore, we can sample this signal at 2 times the highest frequency (200 kHz). The sampling rate is therefore 400,000 samples per second
A complex bandpass signal has a bandwidth of 200 kHz. What is the minimum sampling rate for this signal?
Solution
We cannot find the minimum sampling rate in this case because we do not know where the bandwidth starts or ends. We do not know the maximum frequency in the signal.

## Slide 64: PCM: Quantization
Sampling results in a series of pulses of varying amplitude values ranging between two limits: amin and amax
The amplitude values are infinite between the two limits
Need to map the infinite amplitude values onto a finite set of known values
  This is achieved by dividing the distance between min and max into L zones, each of height 
= (max - min)/L
The midpoint of each zone is assigned a value from 0 to L-1 (resulting in L values)
Each sample falling in a zone is then approximated to the value of the midpoint

## Slide 65
Quantization and Encoding of a sampled signal

## Slide 66
Maximum Voltage Vmax = 20 V
Minimum Voltage Vmin = - 20 V
Figure shows the actual amplitudes (ideal sampling)
Normalized PAM values = actual amplitudes / ∆
Normalized Quantized values = (mid point amplitude in each zone) / ∆
Normalized error = Normalized Quantized values – Normalized PAM values
Quantization code – is based on the quantization levels at the left of the graph
Encoded works – final products of the conversion

## Slide 67
Quantization Zones
Assume a voltage signal with amplitudes
Vmin= - 20V and Vmax = + 20V.
We want to use L = 8 quantization levels
Zone width = (20 – (-20))/8 = 5
The 8 zones are: -20 to -15, -15 to -10, -10 to -5, -5 to 0, 0 to +5, +5 to +10, +10 to +15, +15 to +20
The midpoints are: -17.5, -12.5, -7.5, -2.5, 2.5, 7.5, 12.5, 17.5
Assigning Codes to Zones
Each zone is then assigned a binary code.
The number of bits required to encode the zones, or the number of bits per sample is as follows:
nb = log 2 L
Given our example, nb = 3
The 8 zone (or level) codes are therefore: 000, 001, 010, 011, 100, 101, 110, and 111
Assigning codes to zones:
  000 will refer to zone -20 to -15
  001 to zone -15 to -10, etc.

## Slide 68
Quantization Error
When a signal is quantized, we introduce an error - the coded signal is an approximation of the actual amplitude value.
The difference between actual and coded value (midpoint) is referred to as the quantization error.
The more zones, the smaller  which results in smaller errors.
BUT, the more zones the more bits required to encode the samples -> higher bit rate
Changes the signal-to-noise ratio of the signal
  Reduces upper limit capacity (as per Shannon)
Signals with lower amplitude values will suffer more from quantization error as the error range: /2, is fixed for all signal levels
Non linear quantization is used to alleviate this problem. Goal is to keep SNR fixed for all sample values
SNRdb = 6.02 nb + 1.76 dB
Nb = log 2 L

## Slide 69: What is SNRdb in the previous example?
SNRdB = 6.02(3) + 1.76 = 19.82 dB
A telephone subscriber line must have an SNRdb above 40. What is the minimum number of bits per sample?
SNRdb = 6.02 nb + 1.76 = 40  n = 6.35

## Slide 70
Uniform Versus Nonuniform Quantization
  For many applications, the distribution of instantaneous amplitudes in the analog signal is not uniform
    Amplitude changes more frequently in lower amplitudes than in higher ones
  Hence, use non-uniform zones
    Height of ∆ is not fixed
    ∆ is greater at lower amplitudes and less at higher amplitudes
  Achieved by using a process called companding (at sender) and expanding (at receiver)
    Companding reduces the instantaneous voltage amplitude for large values
      Gives greater weightage to strong signals
      Gives less weightage to weak signals
    Expanding is the opposite of companding
  Effectively reduces SNRdb of quantization

## Slide 71
Encoding
  After each sample is quantized, number of bits per sample is decided
  Each sample is changed to an nb – bit code word
  Number of bits for each sample (nb) is determined by the number of quantization levels (L)
    nb = log 2 L
  Bit rate = sampling rate X number of bits per sample
  Bit rate = fs x nb
We want to digitize the human voice. What is the bit rate, assuming 8 bits per sample?
Solution
The human voice normally contains frequencies from 0 to 4000 Hz. So the sampling rate and bit rate are calculated as follows:

## Slide 72
Original Signal recovery
  Requires PCM decoder
  Decoder uses circuitry to convert the code words into a pulse that holds the amplitude until the next pulse
  Stair-case pulse so created is sent through low pass filter to generate smooth analog signal
    Filter has same cut-off frequency as the original signal at the sender
  If the signal is sampled at the Nyquist sampling rate (or greater), if enough quantization levels are available, original signal will be recreated
  Maximum and minimum values of original signal can be achieved by amplification

## Slide 73
Components of the PCM decoder

## Slide 74
PCM Bandwidth
  Minimum bandwidth of a line-encoded signal
  Bmin = c X N X (1/r)
  Bmin = c X nb X fs X (1/r)
  Bmin = c X nb X 2 X Banalog X (1/r)
  When 1/r = 1 for NRZ or bipolar and c = ½ (the average situation)
    Bmin = nb X Banalog
    Minimum bandwidth of digital signal is nb times greater than the bandwidth of the analog signal
      Price we pay for digitization

## Slide 75
We have a low-pass analog signal of 4 kHz. If we send the analog signal, we need a channel with a minimum bandwidth of 4 kHz. If we digitize the signal and send 8 bits per sample, we need a channel with a minimum bandwidth of 8 × 4 kHz = 32 kHz.

## Slide 76
Maximum Data Rate of a Channel
  Data rate of the channel
  Nmax = 2 X B X log 2 L
Proof:
  Assume that the available channel is low-pass with bandwidth B
  Assume that the digital signal we want to send has L levels, each level is a signal element
  r = 1/log 2 L
  First pass the digital signal through a low – pass filter to cut off the frequencies above B Hz
  Treat the resulting signal as an analog signal and sample it at 2 X B samples per second and quantize it using L levels
    Additional levels are useless as the original signal had L levels
  Resulting bit rate is
  N = fs X nb = 2 X B X log 2 L
  Hence, the maximum bandwidth is
  Nmax = 2 X B X log2L bps
  Minimum Required Bandwidth
  Bmin = N /(2 X log2L) Hz

## Slide 77: Delta Modulation
PCM is a very complex technique
PCM finds value of signal amplitude for each sample | DM finds chane from previous sample
Process of delta modulation

## Slide 78
Components of Delta Modulation
Modulator used at sender site
  Create stream of bits from the analog signal
  Process records small positive or negative changes called delta ()
    Records 1 or 0 respectively
  Process needs a base
  Builds a second signal that resembles a stair case
Hence, finding the change is reduced to comparing the input signal with gradually made staircase signal
Delay unit holds the staircase function for a period between two comparisons

## Slide 79
Components of Delta demodulation
Demodulator used at receiver site
  Takes digital data and, using staircase maker and delay unit, creates analog signal
  The analog signal needs to pass through a low pass filter for smoothing
Adaptive DM
  If  value is not fixed, better performance can be achieved
    Value of  changes according to amplitude of analog signal
Quantization error is introduced
  But, much less than that for PCM

## Slide 80: Transmission modes
Parallel Transmission
Serial Transmission

## Slide 81
Data Transmission Modes

## Slide 82: Parallel Transmission
Parallel Transmission – multiple bits are sent with each clock tick
  Binary data is organized into groups of n bits each
  By grouping, we send data n bits at a time instead of 1
Use n wires to send n bits at one time
Advantage:
  Speed
  Can increase transfer speed by a factor of n over serial transmission
Disadvantage
  Cost
  Hence, limited to short distances

## Slide 83
Parallel Transmission

## Slide 84: Serial Transmission
One bit follows another
  Hence, only one communication channel is needed rather than n to transmit data between two communicating devices
Advantage:
  Reduces cost of transmission over parallel by roughly a factor of n
Since communication within devices is parallel
  Conversion devices are required at interface between sender and the line (parallel – to – serial) and between the line and the receiver (serial – to – parallel)
Serial transmission occurs in
  Asynchronous
  Synchronous
  Isosynchronous

## Slide 85
Serial Transmission

## Slide 86: Serial transmission: Asynchronous Transmission
Timing of the signal is unimportant
Information is received and translated by agreed upon patterns
  Patterns are based on grouping bit stream into bytes
Each group (8 bits) is sent along the link as a unit
Sending system handles each group independently
  Relaying to link without regard to a timer
Without synchronization, receiver cannot use timing to predict when the next group will arrive
To alert receiver, an extra bit (0) is added to beginning of each byte
  Also called start bit
To let receiver know that the byte is finished, 1 or more additional bits are appended to the end of the byte
  Also called stop bits

## Slide 87
In asynchronous transmission, we send 1 start bit (0) at the beginning and 1 or more stop bits (1s) at the end of each byte. There may be a gap between each byte.
Asynchronous here means “asynchronous at the byte level,”
but the bits are still synchronized; their durations are the same.
To transmit 1 byte, at least 10 bits are transmitted
  2 additional bits for control
Transmission of each byte may be followed by a gap of varying duration
This gap can be represented either by an idle channel or by a stream of additional stop bits

## Slide 88
Asynchronous Transmission
Example:
Connection of a keyboard to a computer
  User types only one character at a time
  Extremely slowly in terms of data processing
  Leaves unpredictable gaps of time between characters

## Slide 89: Serial Transmission: Synchronous Transmission
Bit stream is combined into longer frames, which may contain multiple bytes
  Each byte is introduced onto the transmission link without a gap between it and the next one
Left to the Receiver to separate bit stream into bytes for decoding purposes
  Data are transmitted as an unbroken string of 1s and 0s and receiver separates that string into bytes or characters
In synchronous transmission, we need bits one after another without start or stop bits or gaps. It is the responsibility of the receiver to group the bits.

## Slide 90
Synchronous transmission
The divisions shown do not exist
Sender puts data onto the line as long string
If sender puts data in bursts, the gaps must be filled with special sequence of 0s and 1s i.e. to represent an idle channel
Faster than the asynchronous as no extra bits or gaps
More useful for high-speed applications
Byte synchronization is accomplished in the data-link layer
Uneven gaps may be found between frames
Without gaps, start and stop bits, there is no built-in mechanism to help receiving device adjust its bit synchronization midstream.

## Slide 91: Serial Transmission: Isochronous
In real-time audio and video, uneven delays between frames are not acceptable
  Synchronous transmission hence fails
  Guarantees that the data arrive at a fixed rate
Example:
TV images are broadcast at the rate of 30 images per second
They must be viewed at the same rate
If each image is sent by using one or more frames, there should be no delays between frames
Hence synchronization of characters is not enough; the entire stream of bits must be synchronized

## Slide 92: Thank You!!!