## Slide 1: Practice session-1

## Slide 2: Questions
1) what is the largest binary number that can be obtained with 8 bits? What is its decimal equivalent?

## Slide 3
2^8-1=255

## Slide 4
Convert the following binary numbers to decimal:
101110 ;

## Slide 5
101110=46

## Slide 6
Convert the following decimal number to binary, octal and hexadecimal:
7562.45

## Slide 7
1110110001010.01110011
Octal: 16612.3463
hex: 1D8A.73

## Slide 8
F3A7C2 to binary, octal, decimal

## Slide 9
111100111010011111000010
Oct :74723702
Decim:15968194

## Slide 10
Multiply : 101110101*101101=

## Slide 11
373*45= 16785
100000110010001

## Slide 12
101000101-11011101=

## Slide 13
1101000

## Slide 14
211 base x=152 base 8

## Slide 15
7

## Slide 16
Assign unique binary combinations in some orderly fashion to the 52 playing cards. use minimum number of bits.

## Slide 17
00XXXX=Clubs
01XXXX=Hearts
10XXXX=Spades
11XXXX=Diamonds

## Slide 18
XX0000=Ace
XX0001=2
XX0010=3
XX0011=4
XX0100=5
XX0101=6
XX0110=7
XX0111=8
XX1000=9
XX1001=10
XX1010=Jack
XX1011=Queen
XX1100=King

## Slide 19: Practice
1) 110101.11 ; 110110100 to decimal
Answer:110101.11=53.75 ; 110110100=436
2)1938.257 and 175.175 to binary, octal, and hexadecimal
binary:11110010010.01000001110
Octal: 3622.2034, Hex: 792.4C
175.175:
binary: 10101111.00101100110
Octal: 257.1314 Hex: AF.2CC

## Slide 20: Exercise – Convert ...
Don’t use a calculator!
Decimal | Binary | Octal | Hexa- decimal
33 |  |  | 
 | 1110101 |  | 
 |  | 703 | 
 |  |  | 1AF
Answer

## Slide 21: Exercise – Convert …
Decimal | Binary | Octal | Hexa- decimal
33 | 100001 | 41 | 21
117 | 1110101 | 165 | 75
451 | 111000011 | 703 | 1C3
431 | 110101111 | 657 | 1AF
Answer

## Slide 22
Q.1 Find 1’s and 2’s complement of following:-
(a)I0000000 (b) OOOOOOOO
(c) 11011010 (d) 0 11 10110
(e) 10000 101 (f) 1111 111 1.

## Slide 24
Q.2 Find the 9's and the 10's
complement of the following decimal numbers:
(a) 52,784,630 (b) 63,325,600
(c) 25,000,000 (d) 00,000,000.

## Slide 26
Subtraction using 10’s complement
X-Y and Y-X
X = 72532, Y= 3250

## Slide 27: Anwer
a) 69282 b) -69282

## Slide 28
Subtraction using 2’s complement
X-Y and Y-X
X = 1010100, Y= 1000011

## Slide 29
Q. Subtraction using 10’s complement
(a ) 6, 428 - 3,409 b) 125 - 1,8OO
(c) 2,043 - 6,152 (d ) 1,631 - 745

## Slide 30
(a) 3019 (b) -1675 (c) -4109 (d) 886

## Slide 31
Q. Subtraction using 2’s complement
a) 10011 - 10001 b) 100010- 100011
(c ) 1001 - 101000 d) 110000 - 10101

## Slide 32
Answer: a) 00010 b) -000001 c)-011111 d)011011